1.0.0.0

# Prerequisites

- 32-bit Windows 10/7/XP machine

- 4C Card

- 4C Drivers.zip

- Software is available here

# How to Install

- First run WD1290.

- It is only necessary to install the WinDriver Core component, the Development Libraries and Additional Languages may be deselected in this window.

- Unzip 4c.zip.

- Navigate to Control Panel>Device Manager.

- In Device Manager, navigate to Other Devices>Other PCI Bridge Device>Update Driver.

- For Win 7 and 10, Select “Browse my computer for driver software”. For Win XP, select “No not this time”, and then “Install from a specific location (Advanced)”

- For Win 10 and 7 elect “Browse…” and select the unzipped 4c folder. For XP, select “Search for best drivers in these locations”, check “Include this location in the search”, select “Browse” and select the unzipped 4c folder

- Select “Install this driver software anyway”. Upon completion the “PLX_9050” should be visible in Device Manager as shown.

- Driver is now ready for use.

# Text boxes

Measuresoft Development Ltd.

Installation of 3595 4C PCI card on 32-bit Windows 10/7/XP

Version: 1.0.0.0

Measuresoft Development Limited

Partnership Courtyard

The Ramparts

Dundalk

Ireland

Tel + 353 42 933 2399

Fax + 353 42 932 7187

This document is the copyright of Measuresoft, and may not be modified, copied, or distributed in any form whatsoever without the prior permission of Measuresoft

Prepared for Measuresoft by

Fergal Cassidy

Wednesday, January 16, 2019

© Measuresoft Development